## Slide 1
FEASIBILITY & VIABILITY
Coupled Hydro-Meteorological Framework • 0–3 Hour Street-Level Flood Nowcasting • SIH 2026 | PS 26085
POTENTIAL CHALLENGES / RISKS
MITIGATION STRATEGIES
CHALLENGES → MITIGATION
ENGINEERING FEASIBILITY
1
2D SIMULATION LATENCY
Full-city 2D shallow-water solvers can miss the 0–3 h warning window.
1
FAST HYBRID PONDING ENGINE
Vectorized 1D surcharge + DEM depression filling. Target: <350 ms inference.
2
DRAIN SILTATION & CLOGGING
Solid waste and silt reduce inlet / conduit capacity beyond clean-model assumptions.
2
DYNAMIC CLOGGING FACTOR (μclog)
Uses maintenance, desilting and grievance signals to throttle effective capacity.
3
UNMAPPED UNDERGROUND DRAINS
Legacy wards may lack complete digital subsurface network topology.
3
TOPOGRAPHIC FLOW INVERSION
OSM road corridors + DEM flow gradients synthesize a directed drainage graph.
4
RADAR ATTENUATION & DATA GAPS
Ground clutter, beam attenuation and sparse gauges create rainfall uncertainty.
4
MULTI-SOURCE RAINFALL FUSION
Combines radar with satellite/AWS observations to reduce spatial rainfall gaps.
RESULTING FEASIBILITY & VIABILITY
1. TECHNICAL FEASIBILITY
• Zero sensor capex
• Open IMD radar + Cartosat DEM
• Proven models + modern ML
2. OPERATIONAL VIABILITY
• 0–3 h lead-time predictions
• Street-level depth + timing
• Safe A* navigation API
3. ECONOMIC VIABILITY
• Cost-effective open data/tools
• Minimal additional hardware
• Cloud-native deployment
4. PAN-INDIA SCALABILITY
• Calibrated on Chennai
• Portable to Mumbai, Delhi, Bengaluru
• Modular + configurable
SMART INDIA HACKATHON 2026 • PS 26085
PREDICT | VISUALIZE | ALERT